## Slide 1: Modeling Urban Stormwater Using EPA-SWMM
Robert (Bob) Carr, PE, CSM, ENV_SP
Water Resources Modeling, LLC
Robert Dickinson, ME
Innovyze
Austin, TX
January 31 – February 1, 2010
Thanks to David Sample, Ph.D for slide information.

## Slide 2: WORKSHOP GOAL
To provide professionals in the stormwater management field with a detailed understanding of the hydrologic/hydraulic modeling tools in EPASWMM available to support design of practices intended to control and mitigate the negative effects of urban runoff.

## Slide 3
Day 1:
Surface runoff hydrology o Introduction to GUI features and Theory o Runoff and Infiltration Options o SCS methodology
Hydraulic routing o Introduction to GUI features and Theory o Pipe and surface channel modeling o Hydraulic routing using kinematic and dynamic wave algorithms
Advanced Hydrology o Importing hydrographs generated from other models (application) o SCS Hydrographs (supplied by NCIMM as Time Series) o Low Impact Development (LID) stormwater modeling
Advanced Hydraulic o HEC-RAS Natural Sections o Quasi Flood Plain Modeling o Real Time Controls
Detention basin modeling o Ponds o Weirs o Orifices

## Slide 4
Day 2:
Understanding the precision and accuracy of SWMM modeling (presentation from detailed studies of SWMM modeling)
Individualized instruction on specific SWMM modeling capabilities o “Dual-drainage” systems using surface streets as conveyance o Natural Channels o Surface Ponding or Quasi 2D Modeling o Low Impact Development (LID) stormwater modeling o Stormwater quality modeling

## Slide 5: SWMM Model
1-dimensional, hydrologic model
Lumped parameter (as opposed to distributed)
Link-node architecture

## Slide 6: SWMM History
Based upon information from James, W., Rossman, L.A., Huber, W.C., Dickinson, R.E., James, R.C., Roesner, L.A., and Aldrich, J.A., 2005, User’s Guide to SWMM5, Computational Hydraulics International, Ltd, 852 pages.

## Slide 7: SWMM History (Con’t)
Based upon information from James, W., Rossman, L.A., Huber, W.C., Dickinson, R.E., James, R.C., Roesner, L.A., and Aldrich, J.A., 2005, User’s Guide to SWMM5, Computational Hydraulics International, Ltd, 852 pages.

## Slide 8: SWMM Runoff
CONCEPT:
  Developed by the USA EPA as a deterministic approach to runoff
Data Needs
  Drainage Area
  Percent Impervious
  Basin Slope and Width
  Rainfall
  Evaporation
  Infiltration Method
Limitations
  Lumped Catchment Parameters

## Slide 9: Subcatchments
Idealized rectangular catchment
Routing choices
  Pervious (adjacent sub- catchment)
  Impervious (adjacent sub- catchment)
  Outlet
James, W., Rossman, L.A., Huber, W.C., Dickinson, R.E., James, R.C., Roesner, L.A., and Aldrich, J.A., 2005, User’s Guide to SWMM5, Computational Hydraulics International, Ltd, 852 pages.

## Slide 10: Catchment Surfaces

## Slide 11: Runoff Routing from Catchments
Non-linear Reservoir Model
(coupled equations)
  Continuity:
  Where:
  V = A · d = volume of water on the subarea, [L3]
  d = water depth, [L]
  t = time, [T]
  A = surface area of subcatchment, [L2]
  i* = rainfall excess = rainfall/snowmelt intensity minus evaporation, [L/T]
  Q = subcatchment (or subarea) outflow, [L3/T]
  Manning’s Equation (omit 1.49 for SI):
  n = Manning's roughness coefficient,
  d = water depth, [L]
  dp = depth of depression (retention) storage, [L]
  S = slope, dimensionless
Source: Rossman, L., 2016. Storm Water Management Model Reference Manual Volume I – Hydrology, U.S. Environmental Protection Agency, National Risk Management Research Laboratory, Office of Research and Development, 235 p., EPA/600/R-15/162.

## Slide 12: Solving Non-linear Reservoir
Solve in each time step
Used in all calculations (omit 1.49 for SI)
James, W., Rossman, L.A., Huber, W.C., Dickinson, R.E., James, R.C., Roesner, L.A., and Aldrich, J.A., 2005, User’s Guide to SWMM5, Computational Hydraulics International, Ltd, 852 pages.

## Slide 13: What is Subcatchment Width?
L=Measure representative overland flow path
W=A/L
Typically calibration parameter (should be consistent through subcatchments)
Where:
tc = time of concentration, [T]
L = subcatchment length [L],
i* = rainfall excess (rainfall minus losses), [L/T]
a, m = kinematic wave parameters, m=5/3,
flow per unit width [L2/T], and
d = depth of flow, [L]
James, W., Rossman, L.A., Huber, W.C., Dickinson, R.E., James, R.C., Roesner, L.A., and Aldrich, J.A., 2005, User’s Guide to SWMM5, Computational Hydraulics International, Ltd, 852 pages.

## Slide 14: Hydraulic Width Effects
James, W., Rossman, L.A., Huber, W.C., Dickinson, R.E., James, R.C., Roesner, L.A., and Aldrich, J.A., 2005, User’s Guide to SWMM5, Computational Hydraulics International, Ltd, 852 pages.

## Slide 15: Overland Flow Roughness
Similar to channels, but different
James, W., Rossman, L.A., Huber, W.C., Dickinson, R.E., James, R.C., Roesner, L.A., and Aldrich, J.A., 2005, User’s Guide to SWMM5, Computational Hydraulics International, Ltd, 852 pages.

## Slide 16: Depression Storage
Measure of surface storage in uneven depressions
Subject to calibration
James, W., Rossman, L.A., Huber, W.C., Dickinson, R.E., James, R.C., Roesner, L.A., and Aldrich, J.A., 2005, User’s Guide to SWMM5, Computational Hydraulics International, Ltd, 852 pages.

## Slide 17: Infiltration
SCS
P = rainfall, [L]
S = storage after runoff begins, [L]
Ia = initial abstraction=0.2S, [L]
Q = runoff volume @ depth, [L]
Horton
fc = infiltration capacity at time t, [L/t]
k = constant relating the rate of decreasing infiltration capacity, [T-1]
fc = final or equilibrium infiltration capacity, [L/T]
f0 = initial infiltration capacity, [L/T]
James, W., Rossman, L.A., Huber, W.C., Dickinson, R.E., James, R.C., Roesner, L.A., and Aldrich, J.A., 2005, User’s Guide to SWMM5, Computational Hydraulics International, Ltd, 852 pages.

## Slide 18: Infiltration
Green-Ampt
F (t) = accumulated infiltration during time step t, [L]
f (t) = infiltration rate during time step t, [L/T]
K = saturated hydraulic conductivity of layer, [L/TT]
Δθ = η- θi , change in moisture
θi =Soil moisture content
η = porosity
Ѱ = Soil suction head, [L]
Note: IMD lower for single event
Sample, D. and Heaney, J., 2006. Integrated Management of Irrigation and Urban Stormwater Infiltration, J. Water Res. Pl. ASCE, 132 (5): 362-373. 132 (5), 362-373, Available from: http://link.aip.org/link/?QWR/132/362/1.

## Slide 19: Evaporation
Climatology, daily, max, min T
James, W., Rossman, L.A., Huber, W.C., Dickinson, R.E., James, R.C., Roesner, L.A., and Aldrich, J.A., 2005, User’s Guide to SWMM5, Computational Hydraulics International, Ltd, 852 pages.

## Slide 20: Soil Moisture Storage
  ΔS = change in soil moisture storage P = precipitation, [L]
  R = runoff volume, [L]
  ET = evapotranspiration, [L]
Wilting Point
Field Capacity
Depletion
Regeneration
Sample, D. and Heaney, J., 2006. Integrated Management of Irrigation and Urban Stormwater Infiltration, J. Water Res. Pl. ASCE, 132 (5): 362-373. 132 (5), 362-373, Available from: http://link.aip.org/link/?QWR/132/362/1.

## Slide 21: Snowmelt
Accumulation
Melting
Removal
Sample, D. and Heaney, J., 2006. Integrated Management of Irrigation and Urban Stormwater Infiltration, J. Water Res. Pl. ASCE, 132 (5): 362-373. 132 (5), 362-373, Available from: http://link.aip.org/link/?QWR/132/362/1.

## Slide 22: Groundwater
Provides a sink for deep percolation
Necessary for continuous simulation
James, W., Rossman, L.A., Huber, W.C., Dickinson, R.E., James, R.C., Roesner, L.A., and Aldrich, J.A., 2005, User’s Guide to SWMM5, Computational Hydraulics International, Ltd, 852 pages.

## Slide 23: Junctions and Conduits
James, W., Rossman, L.A., Huber, W.C., Dickinson, R.E., James, R.C., Roesner, L.A., and Aldrich, J.A., 2005, User’s Guide to SWMM5, Computational Hydraulics International, Ltd, 852 pages.

## Slide 24: BMP Modeling
Wet/dry Ponds, are modeled as storage nodes
LID BMPs are embedded in subcatchments
  Types:
    Bioretention/Rain garden
    Green roof
    Infiltration trench
    Permeable pavement
    Rain barrels
    Vegetated swales
  Types
    Routing: Pervious:Pervious
    Outflow: Normally to pipe
LID Practice
Subcatchment

## Slide 25: SWMM LID Limitations
BMPs are modeled within subcatchments, not nodes
Routing-pervious to pervious issues
Treatment simplified, mass balance
Infiltration approximation during wetting/drying
LID Practice 2
Subcatchment 2a
LID Practice 1
Subcatchment 1a
Subcatchment 1

## Slide 26: Event-Based Simulation
Event-based
  Uses SCS Type I, IA, II, III rainfall, 24 hours, or real short-duration storm events, including NOAA A-D
    Multiply Weighting factor by storm volume, found at: http://dipper.nws.noaa.gov/hdsc/pfds
  Typically ignore:
    Evapotranspiration
    Groundwater
    Long term soil moisture (but initial conditions are important
  Typically uncalibrated

## Slide 27: Continuous Simulation
Purpose, to review long term trends and system behavior in terms of occurrence frequencies
Requires:
  Hourly or subhourly (15-minute) rainfall, normally for 10 years or more (NWS)
  Climatological data (temperature) for ET simulation (NWS)
    http://gis.ncdc.noaa.gov/map/viewer/#app=cdo
    http://cdo.ncdc.noaa.gov/qclcd/QCLCD?prior=N
    Can use National Stormwater Calculator
  Development of Aquifer storage/groundwater flow
Calibration: normally done if data available

## Slide 28: Applications of SWMM
Designing drainage system components for flood control.
Design of detention facilities for flood control and water quality.
Mapping flood plains of natural channels (SWMM 5 is a FEMA-approved model for NFIP studies).
Designing control strategies for minimizing combined sewer overflows.

## Slide 29: Applications of SWMM (con’t)
Evaluating the impact of inflow and infiltration on sanitary sewer overflows (SSOs).
Generating non-point source pollutant loadings for waste load allocation studies.
Controlling site runoff using low impact development (LID) or green infrastructure (GI).
Evaluating the effectiveness of BMPs for reducing wet weather pollutant loadings.